JOB HAZARD ANALYSIS - Task Specific

Workplace Task to be analyzed:	 Use of Flammable, explosive and toxic gases

Department:

McMaster Job Title:

McMaster Hazard Category:  Physical/ Energy

Hazard Type:  explosive/toxic

JCQ# (if applicable):

Loss Potential Rating (please circle):	  MAJOR     MODERATE     MINOR

*If rated as MAJOR a Standard Operating Procedure (SOP) is mandatory

Required Personal Protective Equipment (please circle): Head Hearing Breathing Eye Hand Foot Knee Full Body

| Sequence of Task | Potential Hazards | Action or Procedure | Required Training |
| --- | --- | --- | --- |
| Read MSDS’s and SOP’s before handling and using |  |  These gases may only be used in a fume-hood or in a well-ventilated laboratory. | WHMIS Gas cylinder training Chemical handling |
| Install appropriate regulator and open valves |  Leakage or escape of flammable gases can produce a serious explosive hazard in a laboratory The larger the cylinder, the greater potential for harm due to leaks etc. |  Gas cylinders, control valves and pressure regulators and gauges should all be used carefully and according to the manufacturers' recommendations. Broken or damaged equipment should not be used but must be replaced. Only equipment that is appropriate i.e. specially designed for use with toxic, explosive or corrosive gases may be used.  The smallest cylinder size that is practicable should be used e.g. a lecture bottle that can be sited in a fume hood. |  |
| Use of gases |  Gases can be reactive e.g oxygen and highly toxic e.g. carbon monoxide. – leaking gas can react with its surroundings ie: equipment, chemicals, skin etc.  "Inert" gases such as nitrogen, carbon dioxide and argon can cause asphyxiation if released in quantity. Containers that receive the gases can explode if not rated to accept the pressure |  There should be a regular check for leaks especially in joints pressure.  Prior to introducing a flammable gas into a reaction vessel, the equipment must be purged of oxygen by evacuation or by flushing with inert gas  Naked flames or other sources of ignition must be rigorously excluded from the vicinity.  Exhaust lines must be properly vented e.g. to a fume hood.  Receiving containers must be capable of accepting the gas at the required operating pressure |  |

# Text boxes

*Supervisor needs to review with worker and both signatures are required below

Date: ___________________________________

Reviewed by Supervisor: ___________________

Employee Signature: _______________________

Supervisor Signature: ______________________